## Slide 1: Machine Learning for Monitoring of Manufacturing Systems
Engineering Informatics Group
4/20/16
Max Ferguson
Notes: Hi, My name is Max Ferguson.
Today I’m going to dive a little deeper into the analysis we have been doing at Stanford University
Show you some really cool things we can do with Machine Learning

## Slide 2: Contents
  Machine Learning for Manufacturing
  Collecting data
  Predicting machine behavior
  Predicting material type
  Predicting tool wear
  Exchanging Machine Learning Models
  Predictive Model Markup Language (PMML)
Looking to the Future
  Identifying sudden failure
  Generalizing tool wear recognition with online learning
  Questions
Notes: Going to by showing you the cool things we can do with vibration and audio data

## Slide 3: Data Collection
Mori Seiki Milling Machine
Operated at 3000 RPM
High feed rate to accelerate tool wear
Infinite Uptime Sensor
3 Axis Acceleration Sensor
Audio Sensor
Waterproof
Notes: We primarily collected data using a Mori Seiki machine in the Berkeley lab.
We used an infinite uptime sensor to collect data

## Slide 4: Raw Data
Vibration data
1000 Hz Sample Rate
3 Axis
Acoustic Data
8000 Hz Sample Rate

## Slide 5: Data Normalization
Raw Data
Signal does not have a zero mean
Audio and vibration data on different scales
Normalized Data
Centered about the x-axis
Signal energy normalized to 1

## Slide 6: Enveloping vibration data
Calculate the RMS combination of vibration signals
Fit a smooth envelope to the RMS combination

## Slide 7: Cut Boundary Extraction
Vibration
Notes: We use a threshold to assign the cut boundaries.
You can see over the length of the tool life the vibration increases, as the tool wears

## Slide 8: Frequency Content of Each Cut
Vibration
Notes: Next we calculate the frequency content of each cut.
This is frequencey

## Slide 9: Frequency Content of Each Cut
Vibration

## Slide 10: Frequency Content of Each Cut
Vibration

## Slide 11: Frequency Content (Rotation Speed)
3000 RPM
Vibration

## Slide 12: Audio Frequency Content
Audio

## Slide 13: Early Observations
  Signal energy increases as tool wears
  Rotation speed can be inferred from the vibration spectra
  There is a notable increase in vibration when the tool is milling

## Slide 14: Identifying Milling Machine Behavior
Machine Learning For Manufacturing

## Slide 15: Extracting Vibration Energy Features
PCA
E
E
E
E

## Slide 16: Principal Components of Signal Energy

## Slide 17: Gaussian Mixture Model Classification

## Slide 18: Conventional and Climb Milling
Conventional Milling
Prone to heat hardening
Often leads to faster blade wear
Climb Milling
Releases more vibration energy, especially at the cutting frequency
Can impose a lot of stress on the milling machine and cutting tool

## Slide 19: Milling Cut Classification

## Slide 20: Milling Cut Classification

## Slide 21: Cut Classification - Conclusion
  We can tell what operation the machine is performing from the vibration and audio data
  Climb cutting releases more vibration energy than conventional cutting
  A simple clustering algorithm can automatically detect machine behavior

## Slide 22: Classifying Material Type
Machine Learning For Manufacturing

## Slide 23: Predicting Material Type
  Milling different materials produces different audio (and vibration) signals
  If sensors can detect material type, they might be able to detect material defects
  Being able to detect material yield strength and elasticity could help to automate quality control
Stainless Steel
A36 Mild Steel
1018 Mild Steel

## Slide 24: Predicting Material Type – Vibration Energy
SVM
Vibration Energy
Material Type
E
E
E
E

## Slide 25: Predicting Material Type - Support Vector Machine
Assume and are on the marginal lines
Reduces an optimization problem:
Width
Primal problem
To find

## Slide 26: Predicting Material Type - Multiclass Support Vector Machine
1018 A36
Stainless Steel Mild Steel
New Sample

## Slide 27: Predicting Material Type – SVM Results
Chart: Classification Accuracy for each Material
| 1018 Mild Steel | A36 Mild Steel | Stainless Steel
Linear | 0.21 | 0.21 | 0.3
Quadratic | 0.73 | 0.67 | 0.78
Gaussian | 0.81 | 0.72 | 0.81
~75 % Classification Accuracy

## Slide 28: Predicting Material Type – Summary
  Achieved 75% accuracy using cut energy
  Very good proof of concept
  Test conditions are constant so we would expect accuracy to be near 100%
  We need more input features to get better classification results

## Slide 29: Extracting More Features – Low Pass Filter
Audio

## Slide 30: Extracting More Features – Band Pass Filter
Audio

## Slide 31: Extracting More Features – High Pass Filter
Audio

## Slide 32: Extracting More Features – Audio Log Scale
Audio

## Slide 33: Extracting More Features – Vibration Log Scale
Vibration

## Slide 34: Predicting Material Type – Energy Bands
~90 % Classification Accuracy

## Slide 35: Predicting Material Type – Conclusion
  Achieved 90% accuracy using the following features:
    Overall vibration and audio energy (4)
    Audio energy in three frequency bands (3)
    Vibration energy in six frequency bands (6)
  Samples from a totally different setup were predicted with 55% accuracy
  The classifier could be useful to recognize material defects

## Slide 36: Tool Wear Prediction
Machine Learning For Manufacturing

## Slide 37: Predicting Tool Wear – Background
  Goal is to predict current state of a milling machine tool
  Tool wear been investigated for 40 years but never generalized
  Some researchers have noted that the audio signal from the milling machine is dependent on the tool condition

## Slide 38: Predicting Tool Wear – What is Wear?
10%
20%
30%
40%
50%
60%
80%
100%

## Slide 39: Predicting Tool Wear – Features
Vibration Energy (1+3)
Band Energy (3+6)
E
E
E
E

## Slide 40: Predicting Tool Wear – Results

## Slide 41: Predicting Tool Wear – Human Labeled Tool Wear
 |  |  |  |  |  |  | Part # |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Tool 1 | 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Tool 2 | 1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |  |  |  | 
Tool 3 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 |  |  | 
Tool 4 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 3 |  |  |  |  |  | 
Tool 5 | 1 | 2 |  |  |  |  |  |  |  |  |  |  |  | 
Tool 6 | 1 | 2 | 2 |  |  |  |  |  |  |  |  |  |  | 
Tool 8 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Tool 10 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |  |  | 
Tool 11 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 3 |  |  |  | 
Tool 12 | 1 | 1 | 1 | 2 | 2 | 2 | 3 |  |  |  |  |  |  | 
Tool 17 | 1 | 2 |  |  |  |  |  |  |  |  |  |  |  | 
Tool 18 | 1 | 1 | 2 |  |  |  |  |  |  |  |  |  |  | 
Tool 19 | 1 | 1 | 1 | 2 | 2 | 3 | 3 |  |  |  |  |  |  | 
Tool 20 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
Tool 21 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
Tool 22 | 1 | 1 | 1 | 2 |  |  |  |  |  |  |  |  |  | 
Tool 23 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
1 - New
2 - Lightly worn
3 - Heavily worn

## Slide 42: Predicting Tool Wear – GP Labeled Tool Wear
 |  |  |  |  |  |  | Part # |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Tool 1 | 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Tool 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 |  |  |  |  | 
Tool 3 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 |  |  | 
Tool 4 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 |  |  |  |  |  | 
Tool 5 | 1 | 2 |  |  |  |  |  |  |  |  |  |  |  | 
Tool 6 | 1 | 2 | 2 |  |  |  |  |  |  |  |  |  |  | 
Tool 8 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2
Tool 10 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |  |  | 
Tool 11 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 3 |  |  |  | 
Tool 12 | 1 | 1 | 1 | 2 | 2 | 2 | 3 |  |  |  |  |  |  | 
Tool 17 | 1 | 2 |  |  |  |  |  |  |  |  |  |  |  | 
Tool 18 | 1 | 2 | 2 |  |  |  |  |  |  |  |  |  |  | 
Tool 19 | 1 | 1 | 2 | 2 | 2 | 3 | 3 |  |  |  |  |  |  | 
Tool 20 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
Tool 21 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
Tool 22 | 1 | 1 | 1 | 2 |  |  |  |  |  |  |  |  |  | 
Tool 23 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
1 - New
2 - Lightly worn
3 - Heavily worn

## Slide 43: Predicting Tool Wear - Summary
  A Gaussian process regression model can be used to predict tool wear
  The Gaussian process regression model gives us a uncertainty measure for all predictions
  Even as a human, it is extremely difficult to quantify tool wear in a way that is consistent

## Slide 44: Exchanging Predictive Models
Max Ferguson
04/28/15
PMML Support for Gaussian Process Regression

## Slide 45: Predictive Models
✓
x
-
  Trained using previous (known) data
  Make predictions based on input values
  Are becoming increasingly powerful
  Predictive Model
E
E
E
E

## Slide 46: Industry Adoption
  1990 – 2000: Huge advances in predictive modeling theory
  2000 – 2010: Computational power is sufficient to justify advanced predictive models
  2010 – 2015: Predictive modeling is used by major advertising networks
  2015 – 2016: Google, Amazon and Microsoft release predictive modeling platforms
  2020: Predictive modeling will be embedded in billions of devices

## Slide 47: Industry Adoption
  Predictive models for manufacturing are being created in research labs and universities right now
  How can these models be used by the industry?
  How can these models be transferred from one person to another?
  How do we load the trained models onto a machine?

## Slide 48: Predictive Model Markup Language (PMML)
PMML AND Gaussian Process Regression

## Slide 49: Introduction to PMML
  Developed by the Data Mining Group (DMG)
  Supported by over 20 Vendors and applications
  Contributions from numerous major players
    NASA
    Open Data Group (ODG)…
  Our Contribution
    Stanford and NIST Collaboration

## Slide 50: Example PMML File
  <?xml version="1.0" encoding="UTF-8"?>
  <pmml xmlns="http://www.dmg.org/PMML-4_3" version="4.3">
  <header copyright="DMG.org" />
  <datadictionary numberoffields="32">
  <datafield datatype="double" name="x1" optype="continuous" />
  <datafield datatype="double" name="x2" optype="continuous" />
  <datafield datatype="double" name="y1" optype="continuous" />
  </datadictionary>
  <gaussianprocessmodel functionname="regression" modelname="Gaussian Process Model">
  <miningschema>
  <miningfield name="x1" usagetype="active" />
  <miningfield name="x2" usagetype="active" />
  <miningfield name="y1" usagetype="predicted" />
  </miningschema>
  <output>
  <outputfield datatype="double" feature="predictedValue" name="MeanValue" optype="continuous" />
  <outputfield datatype="double" feature="predictedValue" name="StandardDeviation" optype="continuous" />
  </output>
  <ardsquaredexponentialkernel gamma="0.15651" noisevariance="0.004691">
  <lambda>
  <array n="31" type="real">1.451760 1.555283 0.939452</array>
  </lambda>
  </ardsquaredexponentialkernel>
  <traininginstances fieldcount="32" istransformed="false" recordcount="725">
  <instancefields>
  <instancefield column="x1" field="x1" />
  <instancefield column="x2" field="x2" />
  <instancefield column="y1" field="y1" />
  </instancefields>
  <inlinetable />
  </traininginstances>
  </gaussianprocessmodel>
  </pmml>

## Slide 51: Gaussian Process PMML Package
  Implemented in MATLAB and Python
  Converts trained Gaussian Process Model to PMML
  Allows predictions to be made from PMML file

## Slide 52: Looking to the Future
PMML AND Gaussian Process Regression

## Slide 53: Exploring PMML Applications
  Load PMML model onto a smart sensor (C++)
  Leverage the power of the cloud: make predictions using the Google Machine Learning Engine
  Publish our tool wear and energy consumption models

## Slide 54: Detecting Sudden Changes to Manufacturing Process
Normal Behavior
Unusual Behavior

## Slide 55: Intelligent Sensor Networks
Notes: Further discussion by Raunak

## Slide 56: Questions?
PMML AND Gaussian Process Regression