## Slide 1: Machine Learning for Monitoring of Manufacturing Systems
Engineering Informatics Group
4/20/16
Max Ferguson

## Slide 2: Contents
Collecting Data from the Machines
  Data Collection
  Data Exploration
  Initial Observations
  Collecting Data from the Machines
  Predicting Machine Behavior
  Predicting Material Type
  Predicting Tool Wear
Looking to the Future
  Identifying sudden changes
  Generalizing Tool Wear recognition with online learning
  Questions

## Slide 3: Data Collection
Machine Learning For Manufacturing

## Slide 4: Data collection
Mori Seiki Milling Machine
Operated at 3000 RPM
High feed rate to accelerate tool wear
Infinite Uptime Sensor
3 Axis Acceleration Sensor
Audio Sensor
Waterproof

## Slide 5: Raw Data
Vibration data
1000 Hz Sample Rate
3 Axis
Acoustic Data
8000 Hz Sample Rate

## Slide 6: Data Normalization
Raw Data
Signal does not have a zero mean
Audio and vibration data on different scales
Normalized Data
Centered about the x-axis
Signal energy normalized to 1

## Slide 7: Data Exploration
Machine Learning For Manufacturing

## Slide 8: Enveloping vibration data
Calculate the RMS combination of vibration signals
Fit a smooth envelope to the RMS combination

## Slide 9: Cut Boundary Extraction

## Slide 10: Frequency Content of Each Cut

## Slide 11: Frequency Content of Each Cut

## Slide 12: Frequency Content of Each Cut

## Slide 13: Frequency Content (Rotation Speed)

## Slide 14: Frequency Content (Rotation Speed)

## Slide 15: Overview of Exploratory Data Analysis
Data Analysis Procedure
  Vibration and acceleration data is collected as time series
  Time series data is separated into individual cuts
  Frequency content of each cut is calculated
Early observations
  Signal energy increases as tool wears
  Rotation speed can be inferred from the vibration spectra
  There is a notable increase in vibration when the tool is milling

## Slide 16: Using Unsupervised Machine Learning to Identify Milling Machine Behavior
Machine Learning For Manufacturing

## Slide 17: Extracting Vibration Features
PCA

## Slide 18: A Mathematical Interpretation of Energy
The truncated Fourier of the signal x(t) from time 0 to T:
Then the power spectral density can be defined:
The power of a certain bandwidth can be defined as:
In discrete form the power of a certain frequency can be defined as:

## Slide 19: Principal Component Analysis – Reducing Features
The first component has to satisfy:
Subsequent components can be calculated:
Image: en.wikipedia.org/wiki/Principal_component_analysis

## Slide 20: Principal Components of Signal Energy

## Slide 21: Gaussian Mixture Model Classification

## Slide 22: Gaussian Mixture Model - Mathematical Background
Optimized with the EM Algorithm:
Expectation step: Calculate the membership value yi,j for each data point xj
Where ai is the mixing coefficient for distribution Yi
Maximization step: Optimize the distribution parameters
In the case where we want to optimize the distribution mean:
Assumes that the data is sampled from a one of several Gaussian distributions
Goal is to find the hidden parameters of each distribution
Can be used to label new data points

## Slide 23: Gaussian Mixture Model – Untrained Cut Classification

## Slide 24: Gaussian Mixture Model – Untrained Cut Classification

## Slide 25: Conventional and Climb Milling
Conventional Milling
Prone to heat hardening
Often leads to faster blade wear
Climb Milling
Releases more vibration energy, especially at the cutting frequency
Can impose a lot of stress on the milling machine and cutting tool

## Slide 26: Overview of Unsupervised Learning
Data Analysis Procedure
  Time series data is separated into individual cuts
  Energy content of each signal is calculated
  PCA is used to reduce the feature dimension from four to two
  The EM algorithm is used to fit a Gaussian mixture model to the data
Early observations
  Climb cutting releases more vibration energy than conventional cutting
  Principle component analysis can reduce dimensionality
  A simple clustering algorithm can detect cut type

## Slide 27: Developing a SVM Classifier for Material Type
Machine Learning For Manufacturing

## Slide 28: Predicting Material Type
  Milling different materials produces different audio (and vibration) signals
  If sensors can detect the type of material that is being milled, they might also be able to detect hard/soft spots in the steel
  Being able to detect material yield strength and elasticity could help to automate quality control
Stainless Steel
A36 Mild Steel
1018 Mild Steel

## Slide 29: Predicting Material Type – Test Conditions
  Three different types of steel were milled
    Stainless Steel
    A36 Mild Steel
    1018 Mild Steel
  The rotation speed was fixed to 3000 RPM
  About 300 cuts were performed using each type of steel
  Audio and vibration signals were measured using a single Infinite Uptime sensor

## Slide 30: Predicting Material Type – Vibration Energy
SVM
Vibration Energy
Material Type

## Slide 31: Predicting Material Type - Support Vector Machine
Assume and are on the marginal lines
Reduces an optimization problem:
Width
Primal problem
To find

## Slide 32: Predicting Material Type - Multiclass Support Vector Machine
1018 A36
Stainless Steel Mild Steel
New Sample

## Slide 33: Predicting Material Type – SVM Results
Chart: Classification Accuracy for each Material
| 1018 Mild Steel | A36 Mild Steel | Stainless Steel
Linear | 0.21 | 0.21 | 0.3
Quadratic | 0.73 | 0.67 | 0.78
Gaussian | 0.81 | 0.72 | 0.81
~75 % Classification Accuracy

## Slide 34: Predicting Material Type – Test Conditions
  Achieved 75% accuracy using cut energy
  Very good proof of concept
  Test conditions are constant so we would expect accuracy to be near 100%
  We need more input features to get better classification results

## Slide 35: Predicting Material Type – More Features

## Slide 36: Predicting Material Type – More Features

## Slide 37: Predicting Material Type – More Features

## Slide 38: Predicting Material Type – More Features

## Slide 39: Predicting Material Type – More Features

## Slide 40: Predicting Material Type – Energy Bands
~90 % Classification Accuracy

## Slide 41: Predicting Material Type – Conclusion
  Achieved 90% accuracy using the following features:
    Overall vibration and audio energy (4)
    Audio energy in three frequency bands (3)
    Vibration energy in six frequency bands (6)
  Samples from a totally different setup were predicted with 50% accuracy
  The material type classifier could be useful to recognize material defects if milling conditions were constant over a long period of time

## Slide 42: Developing a Gaussian Process Regression Model For Tool Wear Prediction
Machine Learning For Manufacturing

## Slide 43: Predicting Tool Wear – Background
  Goal is to predict current state of a milling machine tool
  Tool wear been investigated for 40 years but never generalized
  Some researchers have noted that the audio signal from the milling machine is dependent on the tool condition

## Slide 44: Predicting Tool Wear – Test Conditions
  100+ Parts were milled using 23 Tools
  Tools were used until excessively worn
  476 photos were taken of the tool blades throughout the process
  Audio and vibration signals were measured using a single Infinite Uptime sensor
  Data was processed and separated into 3500 individual cuts
  Each cut was manually assigned a wear value

## Slide 45: Predicting Tool Wear – What is Wear?
10%
20%
30%
40%
50%
60%
80%
100%

## Slide 46: Gaussian Process Regression Model
Gaussian Distribution
Distribution over vectors.
Fully specified by a mean and covariance.
The position of the random variable in the vector plays the role of the index.
Gaussian Process
Distribution over functions.
Fully specified by a mean function and covariance function.
The argument of the random function plays the role of the index

## Slide 47: Gaussian Process Regression Model
Covariance function defines the properties in the function space.
Data points ”anchor” the function as specific locations.

## Slide 48: Predicting Tool Wear – Gaussian Process Model
  The Squared Exponential Kernel
  The ARD Kernel automatically adjusts the length scale of each feature dimension
  Need to optimize free parameters for training data
Random Gaussian Noise in the input values

## Slide 49: Predicting Tool Wear – Features
Vibration Energy (1+3)
Band Energy (3+6)

## Slide 50: Predicting Tool Wear – Results

## Slide 51: Predicting Tool Wear – Summarizing results
  There is a large amount of variance and uncertainty in predicting tool wear at each cut
  Strategy: Average the wear predictions for each part that was made. Use the average tool wear to label the tool condition for each part made

## Slide 52: Predicting Tool Wear – Human Labeled Wear
 |  |  |  |  |  |  | Part # |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Tool 1 | 1 |  |  |  |  |  |  |  |  |  |  |  |  | 
Tool 2 | 1 | 2 | 3 | 3 | 3 | 3 | 3 | 3 | 3 |  |  |  |  | 
Tool 3 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 |  |  | 
Tool 4 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 3 |  |  |  |  |  | 
Tool 5 | 1 | 2 |  |  |  |  |  |  |  |  |  |  |  | 
Tool 6 | 1 | 2 | 2 |  |  |  |  |  |  |  |  |  |  | 
Tool 8 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2
Tool 10 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |  |  | 
Tool 11 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 3 |  |  |  | 
Tool 12 | 1 | 1 | 1 | 2 | 2 | 2 | 3 |  |  |  |  |  |  | 
Tool 17 | 1 | 2 |  |  |  |  |  |  |  |  |  |  |  | 
Tool 18 | 1 | 1 | 2 |  |  |  |  |  |  |  |  |  |  | 
Tool 19 | 1 | 1 | 1 | 2 | 2 | 3 | 3 |  |  |  |  |  |  | 
Tool 20 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
Tool 21 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
Tool 22 | 1 | 1 | 1 | 2 |  |  |  |  |  |  |  |  |  | 
Tool 23 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 

## Slide 53: Predicting Tool Wear – GP Labeled Wear
 |  |  |  |  |  |  | Part # |  |  |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14
Tool 1 | 2 |  |  |  |  |  |  |  |  |  |  |  |  | 
Tool 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 | 3 |  |  |  |  | 
Tool 3 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 3 | 3 | 3 | 3 |  |  | 
Tool 4 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 |  |  |  |  |  | 
Tool 5 | 1 | 2 |  |  |  |  |  |  |  |  |  |  |  | 
Tool 6 | 1 | 2 | 2 |  |  |  |  |  |  |  |  |  |  | 
Tool 8 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2
Tool 10 | 1 | 1 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 | 2 |  |  | 
Tool 11 | 1 | 1 | 1 | 1 | 2 | 2 | 2 | 2 | 3 | 3 |  |  |  | 
Tool 12 | 1 | 1 | 1 | 2 | 2 | 2 | 3 |  |  |  |  |  |  | 
Tool 17 | 1 | 2 |  |  |  |  |  |  |  |  |  |  |  | 
Tool 18 | 1 | 2 | 2 |  |  |  |  |  |  |  |  |  |  | 
Tool 19 | 1 | 1 | 2 | 2 | 2 | 3 | 3 |  |  |  |  |  |  | 
Tool 20 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
Tool 21 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 
Tool 22 | 1 | 1 | 1 | 2 |  |  |  |  |  |  |  |  |  | 
Tool 23 | 1 | 1 | 1 | 2 | 2 |  |  |  |  |  |  |  |  | 

## Slide 54: Predicting Tool Wear - Summary
  A Gaussian process regression model can be used to predict tool wear
  The Gaussian process regression model gives us a uncertainty measure for all predictions
  There is a large amount of noise in tool wear predictions for each cut
  Cut-by-cut predictions can be averaged to give tool wear prediction on a part-by part basis
  Even as a human, it is extremely difficult to quantify tool wear in a way that is consistent

## Slide 55: Looking to the Future
Machine Learning For Manufacturing

## Slide 56: Detecting Sudden Changes to Manufacturing Process
  Sensors would be more useful if they could predict sudden changes to their operating environment
  The sensors would collect samples when the machine was operating correctly
  Sensors would alert the engineers when new behavior was observed

## Slide 57: Detecting Sudden Changes to Manufacturing Process
Normal Behavior
Unusual Behavior

## Slide 58: Intelligent Sensor Networks

## Slide 59: Questions?
PMML AND Gaussian Process Regression

## Slide 60
+
Operating Correctly?
Yes
No
Machine 1